## Slide 1
The goal of our project was to create a device that can prevent drowning tragedies from occurring. Our device weigh roughly 16 lbs., but can be configured to meet other standards. By placing this device in your private pool, any handheld device synchronized with the pool alarm will receive an alert indicating when a child has fallen into the pool.
Abstract
Pool Safety Standards
Final Design
We, all members of the pool safety team, have all agreed to donate our widget
to Auburn University for the purpose of inspiring a new age of engineering.
Disposition
Testing Procedure
Certain US states require pool alarms
  Tennessee’s Katie Beth Law
    Requires device to emit alarm of minimum 50dB
    Requires device to detect disturbance caused by 15lb object
  Florida has strict building codes concerning residential pools
ASTM F2208-08 Standard Specification for Pool Alarms
  The device should emit 85dB at a range of 10ft
  No known laws for devices communicating via push notifications
UL Standard for General-Purpose Signaling Devices and Systems and Consumer Product Safety Commission both have published guidelines
Total Costs
(1) Solar Panel: $29.00
(1) DC/Lithium-poly Charger: $17.50
(1) Lithium-poly Battery: $14.95
(1) Powerboost 500: $9.95
(1) Accelerometer: $16.30
(1) Raspberry Pi: $54.99
(1) Chlorine Dispenser: $9.00
Chlorine Dispenser Modifications: $35.00
Shipping costs: $19.12
Total Cost: $205.81
Step 1: Take J.U.I.C.Y to an available pool.
Step 2: Run the python program and store output.
Step 3: Run multiple tests by throwing an object with weight similar to an average toddler into the pool (i.e. 2 gallon jugs filled with water).
Step 4: Adjust thresholds in detection algorithm based on data from experiments.
Marco Zuniga, Cole Graviett, Joe Driscoll, Kaidi Ding, LaShae Timmerman
Matthew Cather, Viraj Patel
Department of Electrical and Computer Engineering, Auburn University, Auburn, Alabama, USA
References
[1] “Drowning." Centers for Disease Control and Prevention. 15 September 2017.
https://www.cdc.gov/healthcommunication/toolstemplates/entertainmented/tips/Drowning.html
[2] “Unintentional Drowning: Get the Facts." Centers for Disease Control and
Prevention. 28 April 2016. https://www.cdc.gov/homeandrecreationalsafety/water-safety/waterinjuries-
factsheet.html
[3] “Risk of Pet Drowning on the Rise!" petplace. 10 December 2014.
https://www.petplace.com/article/dogs/pet-health/risk-of-pet-drowning-on-the-rise/
[4] “A beginner's guide to accelerometers" Dimension Engineering. Date Unknown.
J.U.I.C.Y: Pool Safety Alarm